## Slide 1: Redfish signed measurements
Last updated: 09/23/2021
Vidya Satyamsetti - Google
Jeff Andersen - Google

## Slide 2
SoC
SoC
Use case - Machine attestation
Integrated RoT
RoT
Flash
Integrated RoT
RoT
Flash
Control plane attestation challenger
BMC / daemon
RoT
Flash
Platform policy
Enumerates expected identities and measurements for each device on the machine.
BMC / daemon
BMC / daemon

## Slide 3
*
Requirement - Collect signed measurements from SPDM/TPM Responder
BMC (SPDM Requester /TPM client)
RoT (SPDM Responder/TPM)
Attestation challenger + verifier
Provide challenge;
Get signed measurements
‘Attest to measurements’
Attestation, measurements

## Slide 4
Surfacing signed measurements
BMC
zzzz zRoT
Attestation challenger + verifier
EEPROM
Measure
Redfish
SPDM/TPM
Redfish
Server
(OData via HTTP/Json)
SPDM
Requester
(Byte scheme over MCTP) /TPM client
SPDM
Responder/TPM

## Slide 5
Persisting signed measurements
BMC
RoT
Signature verifier
EEPROM
Measure
SPDM
SPDM
Requester
(Byte scheme over MCTP) /TPM client
SPDM
Responder
Storage
Persist
Signature
Collect and verify signature
Challenger
Provide challenge
Notes: BMC is illustrative. Could be any component with a Redfish server. Ex: BIOS

## Slide 6
SPDM + Redfish today
BMC(Redfish Responder+ SPDM Requester)
RoT(SPDM Responder)
Measurement Blocks
[{
“Index”: 1, “Type”: 0, Size: 0x100, Measurement: ...
},
{
“Index”: 2, “Type”: 0, Size: 0x400, Measurement: ...
}]
SPDM
GET /redfish/v1/??/??/Certificates
Redfish
GET /redfish/v1/??/??/Measurements
Certificates
Measurements (no signature)
GET_CERTIFICATE
GET_MEASUREMENTS
GET_VERSION
GET_CAPABILITIES
NEGOTIATE_ALGORITHMS

## Slide 7
SPDM GET_MEASUREMENTS signature
SPDM Requester
SPDM Responder
Measurements Blocks
[{
“Index”: 1, “Type”: 0, Size: 0x100, Measurement: ...
},
{
“Index”: 2, “Type”: 0, Size: 0x400, Measurement: ...
}]
GET_MEASUREMENTS (Index=0xFF, Offset=0)
MEASUREMENTS (Measurements)
GET_MEASUREMENTS (Index=0xFF, Offset=0x200)
MEASUREMENTS (Measurements)
Signature = Sign(all exchanged requests + responses)

## Slide 8
Surfacing SPDM signature to Verifier - problems
Redfish doesn’t provide a way for an external verifier challenging an SPDM Responder for its measurements.
  Verifier needs to assume SPDM Requester passed in a valid challenge and got a signature.
Notes: It is currently hard for anyone but the SPDM Requester to validate SPDM signatures. Hard to transmit signatures to off-machine components, and also hard to commit signatures to storage.

## Slide 9
Proposal - New Redfish action to sign measurements
Requirements:
  Should support both SPDM and TPM.
  Various parameter constraints must be discoverable by the caller.

## Slide 10
Proposal - New Redfish action(SignMeasurements)
POST /redfish/v1/{Resource}/{ResourceId}/SignMeasurements
  ActionInfo enables discovery of allowed parameters
Resource is the SPDM Responder/TPM
  The resource a new RoT resource being defined in Redfish that can be either an SPDM responder or a TPM
Assumption is that the Redfish server is itself the SPDM Requester or TPM client

## Slide 11
Proposal - SignMeasurements action
<Action Name="SignMeasurements" IsBound="true">
<Parameter Name="Nonce" Type="Edm.String">
<Annotation Term="OData.Description" String="Hex string. Should be unique."/>
<Annotation Term="Validation.Pattern" String="^[0-9a-fA-F]+$"/>
</Parameter>
<Parameter Name=“SigningKeyId” Type=“Edm.Int64">
<Annotation Term="OData.Description" String=“An id of the key to be used for signing measurements. Corresponds to slot id for SPDM and sighandle for TPM”/>
</Parameter>
<Parameter Name="MeasurementIndices" Type="Collection(Edm.Int64)" >
<Annotation Term="OData.Description" String="Array of indices for measurement.”/>
</Parameter>
<Parameter Name="SignerVersion" Type="Edm.String">
<Annotation Term="OData.Description" String=“Version of the signer protocol to be used for signing. Ex: 1.2, 2.0”/>
</Parameter>
<Parameter Name="HashingAlgorithm" Type="Edm.Int64">
<Annotation Term="OData.Description" String=“Hashing algorithm to be used for generating the signed statement"/>
</Parameter>
<Parameter Name="SigningAlgorithm" Type="Edm.Int64">
<Annotation Term="OData.Description" String="Signing algorithm to be used for generating the signed statement."/>
</Parameter>
<ReturnType Type="SoftwareInventory.v1_5_0.SignMeasurementsResponse" Nullable="false"/>
</Action>
</Schema>

## Slide 12: Proposal - SignMeasurements response
*
<ComplexType Name="SignMeasurementsResponse">
<Property Name="CertificateUri" Type=“Certificate.Certificate" Nullable=”false”>
<Annotation Term="OData.Description" String="OData URI of the certificate used to sign measurements."/>
</Property>
<Property Name="SignerProtocol" Type="Enum" Nullable=”false”>
<Annotation Term="OData.Description" String=“SPDM/TPM" />
</Property>
<Property Name="SignerVersion" Type="Edm.String" Nullable=”false”>
<Annotation Term="OData.Description" String="Version of the signer protocol used for signing. Ex: 1.2, 2.0"/>
</Property>
<Property Name="HashingAlgorithm" Type=“Edm.Int64” Nullable=”false”>
<Annotation Term="OData.Description" String=“Hashing algorithm used for generating the signed statement”/>
</Property>
<Property Name="SigningAlgorithm" Type=“Edm.Int64" Nullable=”false”>
<Annotation Term="OData.Description" String="Signing algorithm used for generating the signed statement.”/>
</Property>
<Property Name="SignedMeasurements" Type="Edm.String" Nullable=”false”>
<Annotation Term="OData.Description" String="Hex encoded attestation generated by the signer."/>
</Property>
</ComplexType>
Notes: Red - Indicates additions to existing measurement complex type
Measurements is an array because MeasurementIndex in request can be 0xFF which can mean all. It could be empty also if MeasurementIndex is 0.
Additional_data[0] and algorithms are chosen by BMC but included under signature.

## Slide 13: SignedMeasurements
What does SignedMeasurements represent?
  For TPM, it will be Concatenate(TPMS_ATTEST, TPMT_SIGNATURE)
  For SPDM it is the L2 string
    For SPDM 1.1 and below, L2 = Concatentate(GET_MEASUREMENT0, MEASUREMENTS0, … GET_MEASUREMENTSN, MEASUREMENTSN) where only MEASUREMENTSN contains the signature
    For SPDM 1.2 and above, L2 = Concatentate(VCA, GET_MEASUREMENT0, MEASUREMENTS0, … GET_MEASUREMENTSN, MEASUREMENTSN) where only MEASUREMENTSN contains the signature, VCA is the version, capabilities and algorithms exchanged b/w the Requester and Responder

## Slide 14: Implementation specifics
Definition for SPDM 1.0 and 1.1
SPDM Requester(BMC) shall negotiate VCA based on input SignerVersion, HashingAlgo, SigningAlgo parameters
  May issue a fresh VCA or use existing negotiated state
SPDM Requester(BMC) shall issue one GET_MEASUREMENTS request for every requested measurement index
  For all but the final measurement index, the Requester shall set Param1[0] = 0 (NoSignature)
  For the final measurement index, the Requester shall set Param1[0] = 1 and Nonce to the SignMeasurements request nonce. (Signature)
    If the negotiated version is 1.1, Requester shall set SlotIdParam[3:0] to the slot number(SigningKeyId)
SPDM Requester(BMC) shall set SignedMeasurements to a concatenation of all GET_MEASUREMENTS / MEASUREMENTS messages exchanged with the Responder

## Slide 15: Implementation specifics
Definition for SPDM 1.2
SPDM Requester(BMC) shall ensure that an active SPDM session exists
  May issue a fresh VCA handshake or use a pre-established session
  Must ensure that the VCA handshake contents are preserved in memory till the request is serviced or even after that if re-using the same sessions
SPDM Requester(BMC) shall issue one GET_MEASUREMENTS request for every requested measurement index
  For each request, the Responder shall set RawBitStreamRequested = 0
  For all but the final measurement index, the Requester shall set SignatureRequested = 0
  For the final measurement index, the Requester shall set SignatureRequested = 1, Nonce to the SignMeasurements request nonce, and SlotIdParam[3:0] to the slot number corresponding to the SigningKeyId in the request
SPDM Requester(BMC) shall set AttestationString to a concatenation of VCA, followed by all GET_MEASUREMENTS / MEASUREMENTS messages exchanged with the Responder

## Slide 16
Cache negotiated state (VCA)
Requester
Responder
Redfish
GET_VERSION
GET_CAPABILITIES
NEGOTIATE_ALGORITHMS
GET_DIGESTS
GET_CERTIFICATES
SPDM
GET_MEASUREMENTS0 (No Sig)
GET_MEASUREMENTS1 (No Sig)
…
GET_MEASUREMENTSN (Sig)
POST /redfish/v1/??/??/SignMeasurements
{
Nonce,
MeasurementIndices,
SigningKeyId
}
Signed Measurements (L2 string + signature)
SPDM attestation over Redfish (Requester has cached state)
Notes: MeasurementId should correspond to DSP0274 Ids

## Slide 17
Negotiated state not cached
Requester
Responder
Redfish
GET_VERSION
GET_CAPABILITIES
NEGOTIATE_ALGORITHMS
GET_DIGESTS
GET_CERTIFICATES
SPDM
GET_VERSION
GET_CAPABILITIES
NEGOTIATE_ALGORITHMS
GET_MEASUREMENTS0 (No Sig)
GET_MEASUREMENTS1 (No Sig)
…
GET_MEASUREMENTSN (Sig)
POST /redfish/v1/??/??/SignMeasurements
{
Nonce,
MeasurementIndices,
SigningKeyId,
SignerVersion,
HashingAlgo,
SigningAlgo
}
Signed Measurements (L2 string + signature)
SPDM attestation over Redfish (No cached state)
Notes: MeasurementId should correspond to DSP0274 Ids

## Slide 18: SPDM attestation over Redfish (Destroying cached state)
Negotiated state (+ VCA)
BMC
RoT
Redfish
GET_VERSION
GET_CAPABILITIES
NEGOTIATE_ALGORITHMS
GET_DIGESTS
GET_CERTIFICATES
SPDM
GET_VERSION
GET_CAPABILITIES
NEGOTIATE_ALGORITHMS
GET_MEASUREMENTS0 (NoSig)
….
GET_MEASUREMENTSN (Sig)
POST /redfish/v1/??/??/SignMeasurements
{
Nonce,
MeasurementId,
SigningKeyId,
SignerVersion,
HashingAlgo,
SigningAlgo
}
Signed Measurements (L2 string + signature)
New Negotiated state (VCA)

## Slide 19: Discovery of allowed values for each Parameter
Nonce - No discovery needed
MeasurementIndices - From ActionInfo (For SPDM 0-255)
HashingAlgo/SigningAlgo: 3 paths; any one can be chosen by an implementation
  BMC makes various SPDM NEGOTIATE_ALGO calls to figure out all algos the Responder supports at boot time and provides them in ActionInfo
  Verifier knows what algos Responder uses out-of-band; BMC allows any algorithm to be passed in Redfish request but rejects them if Responder doesn’t support it
  BMC doesn’t like to disturb the existing negotiated state and so allows only one algo; the same is expressed in ActionInfo
SignerVersion: Same as algo but for SPDM GET_VERSION request
SigningKeyId - From ActionInfo, there are a list of allowed values

## Slide 20
Cached sighandle
Requester
Responder
Redfish
TPM
QUOTE
SIGN
NV_READ (for reading EK certificate)
POST /redfish/v1/??/??/SignMeasurements
{
Nonce,
MeasurementIndices,
SigningKeyId,
HashingAlgorithm
}
QUOTE response
TPM attestation over Redfish
TPM_CREATE
Notes: MeasurementId should correspond to DSP0274 Ids

## Slide 21: Discovery of allowed values for each Parameter
Nonce - No discovery needed
MeasurementIndices - From ActionInfo (For TPM 0-31)
HashingAlgo/SigningAlgo: From ActionInfo, there are a list of allowed values
SignerVersion: Fixed by TPM (2.0 etc.)
SigningKeyId - From ActionInfo, there are a list of allowed values

## Slide 22
Signer protocol discovery
There will be a complex property on the Responder resource to indicate an SPDM or TPM Responder

## Slide 23: End of slides